## Slide 1: Digital Communications: Introduction
Sedat Görmüş, PhD

## Slide 2: Outline
Introduction
  Communication System Components(Recap)
  Communication Process (Recap)
  Telecommunication (Recap)
  Wireless Communications (Recap)
  Communication Channels
    Wireless Electromagnetic Channels
    Acoustic Channels
    Storage Channels
  Mathematical Models for Communication Channels
    Additive Noise Channel
    The Linear Filter Channel
    The Linear Time Variant Filter Channel
  Historical Perspective in the Development of Digital Communications

## Slide 3: Communication System Components (Recap)
Source
Coder
Channel
Coder
Modulation
+
Source
decoder
Channel
decoder
demodulation
Distortion and noise
transmitter
channel
receiver
Source
input
Reconstructed
Signal
output
D/A
A/D

## Slide 4: Communication Process (Recap)
Message Signal
Symbol
Encoding
Transmission
Decoding
Re-creation
Broadcast
Point to Point

## Slide 5: Telecommunication (Recap)
Telegraph
Fixed line telephone
Cable
Wired networks
Internet
Fiber communications
Communication bus inside computers to communicate between CPU and memory

## Slide 6: Wireless Communications (Recap)
Satellite
TV
Cordless phone
Cellular phone
Wireless LAN, WIFI
Wireless MAN, WIMAX
Bluetooth
Ultra Wide Band
Wireless Laser
Microwave
GPS
Ad hoc/Sensor Networks

## Slide 7: Analog v.s. Digital ADC/DAC
Common Misunderstanding: All of the transmitted signals are analog. We don’t do digital transmission over the air
Analog-to-Digital Conversion (ADC) and Digital-to-Analog Conversion (DAC) are the processes that allow digital computers to interact with these everyday signals.
Digital information is different from its continuous counterpart in two important respects: it is sampled, and it is quantized

## Slide 8: Source Coder
Examples
  Digital camera: encoder; TV/computer: decoder
  Camcorder
  Phone
  Read the book
Theorem
  How much information is measured by Entropy
  More randomness, high entropy and more information

## Slide 9: Communication Channels
Wireless Electromagnetic Channels
  Electromagnetic energy coupled to the propagation medium by an ANTENNA.
  There is a relation between the antenna aperture size and the signal frequency.
  And antenna must be longer than the 1/10th of the wavelength.
  Example
    If f = 1 Mhz the corresponding wavelength is c/fc = 300 m.
    What would be the minimum antenna height for such am electromagnetic wave.
  Three modes of propagation in the atmosphere.
    Ground-wave propagation
    Sky-wave
    Line-of-Sight (LOS)
  Signal suffers from Several Channel impairments during Propagation
    Multi-path : When the transmitted signal arrives at the destination through multiple propagation paths at different delays.
    Multi-Path-Fading : If the multi-path signal components adds destructively, this results in fading.
    Atmospheric noise and thermal noise
  In general LOS propagation of signal in LF is limited by the curvature of the earth.
    The signal propagation limit is related to the height of the antenna assuming no physical obstructions. And it is km.

## Slide 10: Acoustic Channels
Electromagnetic Waves do not propagate well in the water except low frequencies.
Underwater acoustic communication is a technique of sending and receiving message below water.
Under water acoustic channel is characterized by factors like multi-path propagation, time variations of the channel, small available bandwidth and strong signal attenuation, especially over long ranges.
There are several ways of employing such communication but the most common is using hydrophones.
In underwater communication there are low data rates compared to terrestrial communication, since underwater communication uses acoustic waves instead of electromagnetic waves.

## Slide 11: Storage Channels
Examples are magnetic tape, video and audio tapes, magnetic disks.
The process of storing data on magnetic tape is equivalent to transmitting data over wireless channels.

## Slide 12: Mathematical Models for Communication Channels
The Additive Noise Channel:
  The simplest mathematical model.
  The transmitted signal is corrupted by an additive random noise process
  The additive noise may arise from electronic components and amplifier at the receiver.
  Or interference encountered in transmission.
  If the noise comes from the components, can be classified as thermal noise which is modelled by a Gaussian random process. And called Gaussian noise channel.
  This model is mathematically tractable and most systems suffer from such Nosie.
  Therefore, most analysis take advantage of this model.
  Where is the channel attenuation factor

## Slide 13: Mathematical Models for Communication Channels
The Linear Filter Channel :
  In some physical channel, such as wireline telephone channels, filters are used to ensure that the transmitted signal do not exceed specified bandwidth (this is also true for wireless channels).
  Such channels are generally modelled mathematically as linear filter channels.
  Where c(t) is the impulse response of the linear filter and denotes convolution
+
Linear filter c(t)
Channel
n
r
=

## Slide 14: Mathematical Models for Communication Channels
The Linear Time-Variant Filter Channel :
  Physical channels, such as under-water acoustic channels and ionospheric radio channels are subjected to time-variant multi-path propagation.
  Such channels may be modelled mathematically as time variant filters.
  Such channels are characterised by a time-variant channel impulse response where is the response of the channel at time t due to impulse applied at time .
  represents the elapsed-time variable.
+
Linear Time-variant filter c(t: )
Channel
n
r
=

## Slide 15: The Linear Time-Variant Filter Channel (Cont.)
A good model for multipath signal propagation through physical channels such as the ionosphere (at frequencies below 30 MHz) and mobile cellular radio channels is a special case of The Linear Time-Variant Filter Channels which the time variant impulse response has the form
Where {} represents the possibly time-variant attenuation factor for the L multipath propagation paths and {} are corresponding time delays.
If we substitute this formula in to the linear time –variant filter channel formula we get.
Received signal consists of L multipath components where each component attenuated by {} and delayed by {}

## Slide 16
Historical Perspective : Shannon Capacity
Shannon Theory
  It establishes that given a noisy channel with information capacity C and information transmitted at a rate R, then if R<C, there exists a coding technique which allows the probability of error at the receiver to be made arbitrarily small. This means that theoretically, it is possible to transmit information without error up to a limit, C.
  The converse is also important. If R>C, the probability of error at the receiver increases without bound as the rate is increased. So no useful information can be transmitted beyond the channel capacity. The theorem does not address the rare situation in which rate and capacity are equal.
Shannon Capacity

## Slide 17
Modulation
Process of varying a carrier signal in order to use that signal to convey information
  Carrier signal can transmit far away, but information cannot
  Modem: amplitude, phase, and frequency
  Analog: AM, amplitude, FM, frequency, Vestigial sideband modulation, TV
  Digital: mapping digital information to different constellation: Frequency-shift key (FSK)

## Slide 18: Example
Figure 1.6 page 12
Modulation over carrier fc
s(t)=Accos(2fct) for symbol 1; -Accos(2fct) for symbol 0
Transmission from channel
x(t)=s(t)+w(t)
Correlator
Decoding
  If the correlator output yT is greater than 0, the receiver output symbol 1; otherwise it outputs symbol 0.

## Slide 19: Channel Coding
Purpose
  Deliberately add redundancy to the transmitted information, so that if the error occurs, the receiver can either detect or correct it.
Source-channel separation theorem
  If the delay is not an issue, the source coder and channel coder can be designed separately, i.e. the source coder tries to pack the information as hard as possible and the channel coder tries to protect the packet information.
Popular coder
  Linear block code
  Cyclic codes (CRC)
  Convolutional code (Viterbi, Qualcom)
  LDPC codes, Turbo code, 0.1 dB to Channel Capacity

## Slide 20: Quality of a Link (service, QoS)
Mean Square Error
Signal to noise ratio (SNR)
  Bit error rate
  Frame error rate
  Packet drop rate
  Peak SNR (PSNR)
  SINR/SNIR: signal to noise plus interference ratio
Human factor

## Slide 21: Thank You for Your Attention.