## Slide 1: Wireless Sensor Networks: An Introduction
Sedat Görmüş, PhD

## Slide 2: Outline
A truly connected World vision.
What are the motivated factors?
  The market value & trends.
  Challenges & opportunities.
What are wireless sensor networks?
Mote Platforms.
  What is a mote &What does it contain?
  Popular platforms & evolution
Unique characteristics/challenges.

## Slide 3: An IoT Vision
Source: http://www.opinno.com/en/content/internet-things-0, retrieved: December 2014.
Notes: İnternete bağlı cihaz sayısı günümüzde hızla artmakta. Her ne kadar ana trend mobil cihazlar gibi gözükse de, küük cihazların internete bağlanması hızla gerçek hale geliyor.
Bağlantılar :
    IPv6’e converge edecek.
    Cloud service kullanacak.
    Third party anonymisation ve aggregation serviceleri olacak.
    Ve bağlantılar iki yönlü olacak (Buz dolabınızda meyve olup olmadığını kontrol etmek gibi)

## Slide 4
Chart: Internet of Things Value Added by 2020 (1.9 Trillion Dollars)
| Manufacturing | Healthcare providers | Insurance | Banking | Retail | Computing | Government | Trasport | Utilities | Real Estate | Agriculture | Others
Internet of Things Value Added by 2020 (1.9 Trillion Dolars) | 0.15 | 0.15 | 0.11 | 0.1 | 0.08 | 0.08 | 0.07 | 0.06 | 0.05 | 0.04 | 0.04 | 0.03
Motivation
WSNs gaining importance as new applications are emerging (e.g. m-Health, Smart City and Smart Grid).
Majority of these applications will have many sensors connected to the Internet forming Internet of Things (IoT).
The traffic generated by IoT will constitute a large part of the future internet traffic.
This will necessitate clever solutions and killer applications that will constitute the backbone of the next generation internet.
Notes: Internete bağlı cihazlar exponnansiyel olarak artıyor. (nefes al. Yavaş)
Bu cihazların yarattığı data trafiği ve bu trafiğin güvenli bir şekilde hedefe ulaştırılması büyük fırsatlar sunuyor. (nefes al)
Yeni startuplar, bu yeni fenomenin getirdiği fırsatlardan faydalanmak için oluşturuluyor. (örn. Thingsquare, contiki).
ARGE ve Yeni ürünler için büyük fırsatlar hala mevcut.
--------- ikinci slayt
Internet of things farklı alanlarda fırsatlar sunuyor.
Özellikle:
  Smart City/Community. (Toshiba Tokyo smart grid Project, 3ehouses, etc.)
  Helthcare (Toshiba silmee)
  Factory automation
------------------------
  Bu söylediklerimin bir özeti. (in network aggregation ve storage önem kazanıyor).

## Slide 5: What are wireless sensor networks (WSNs)?
Networks of typically small, battery-powered, wireless devices.
  On-board processing,
  Communication, and
  Sensing capabilities.
Sensors
Processor
Radio
Storage
P
O
W
E
R
WSN device
schematics

## Slide 6: Wireless modules or motes
They are the key ingredients of the a sensor network
  Can communicate
  Can Sense
  Can be reprogrammed
Examples : Mica2, Cricket, MicaZ, Iris, Telos, SunSPOT, Imote2

## Slide 7: Mote Evolution

## Slide 8: Example Mote Platforms & Hardware

## Slide 9
Design Challenges
Why are WSNs challenging/unique from a research point of view?
Typically, severely energy constrained.
  Limited energy sources (e.g., batteries).
  Trade-off between performance and lifetime.
Self-organizing and self-healing.
  Remote deployments.
Scalable.
  Arbitrarily large number of nodes.

## Slide 10
Design Challenges (Cont’d)
Heterogeneity.
  Devices with varied capabilities.
  Different sensor modalities.
  Hierarchical deployments.
Adaptability.
  Adjust to operating conditions and changes in application requirements.
Security and privacy.
  Potentially sensitive information.
  Hostile environments.

## Slide 11: Standardisation Efforts
The platforms are heterogenious, hence many protocols at different layers of the protocol stack.
There is a clear need for standardisation :
  Examples :
    IEEE 802.15.4 (PHY) ,
    Zigbee, WirelessHART, WINA, SP100.11a and 6Tisch (MAC and Above layers)
    6LowPAN (Routing and Internet)
  All these upper layer standards work on top of 802.15.4 PHY
  We will briefly talk about important upper layer standards (ZigBee, WirelessHART and 6LowPAN)

## Slide 12: ZigBee
Important ZigBee != 802.15.4
  ZigBee Works on top of the IEEE 802.15.4 PHY/MAC and defines the remaining layers.
Five application Areas
  Home automation.
  Smart energy.
  Building automation.
  Telecommunication services.
  Personal health care.
Three traffic types
  Periodic data (reporting)
  Intermittent data (event driven)
  Low latency (critical)

## Slide 13: Zigbee Cont.
ZigBee network layer provides connectivity and management functions
  Devices are put into categories based on their functions in the network
    Full Function Devices (FFD) : Can route others data.
    Reduced Function Devices (RFD) : Can be only leaf nodes in the network and generally do sensing and actuating functions.
ZigBee Networking allows devices to move between networks, hence they have flexible addressing mechanisms (Recently ZigBee IP(v6))
Network layer is also responsible for synchronisation, routing and membership (authentication ) functions.
ZigBee Application Layer defines two types of objects namely ZigBee Device Objects (ZDOs) and Manufacturer Defined Application Objects.
  Application is implemented through the manufacturer defined application objects similar to APIs.
  And ZDOs provide networking functions such as role in the network and authentication.

## Slide 14: WirelessHART
Wireless extension to the industry standard Highway Addressable Remote Transducer (HART) protocol.
  HART is a field tested technology and widely used.
  The deployment numbers are above 20 million.
  It is based on superimposing a digital FSK-modulated signal on top of the 4–20mA analog current loop between different components.
  Based on master/slave architecture where up to two masters are accommodated in the network.
WirelessHART is released as part of HART 7 specification as the first open communication standard for control and monitoring applications.
  It relies on IEEE 802.15.4 PHY standard.
  MAC layer is a TDMA mac where bandwidth resources are orthogonalised.

## Slide 15: WirelessHART Network Architecture
Notes: The network manager maintains operation of the network by scheduling
communication slots for devices.
Determining routing tables, and monitoring the health of the network.
The WirelessHART adapters provide backward compatibility by integrating existing HART field devices with the wireless network
At the network layer, table-based routing is used so that multiple redundant paths are established
during network formation and these paths are continuously verified.
Accordingly, even if a communication path between a WFD and a gateway is corrupted, alternate paths are used to provide network
reliability greater than 3σ (99.7300204%).

## Slide 16: 6LowPAN
To enable IP based End-to-End Communication, IETF have devised a standard to bring IPv6 based routing to Wireless Sensor Networks.
  This standard enables small devices to be part of the Internet paving the way for global Internet of Things (IoT).
  The main challenge to squeze 40 byte IPv6 header into a standard (IEEE 802.15.4) which has only a maximum payload of 127 bytes.
  Furthermore, IPv6 supports a payloads of 1280 bytes. Hence an adaptation layer is required to make these two standards work together.
  The adaptation layer is responsible for compressing IPv6 header and fragment and defragment large data payloads.
Instead of sending a single header containing every bits of information 6LowPAN makes use of four different headers as given in the text to optimise the IPv6 header.

## Slide 17: A WSN Protocol Stack with 6LowPAN

## Slide 18: Software
There are several software solutions and operating systems for WSNs
  TinyOS from UC Berkeley.
    Open BSD Licence
    In cooperation with Intel Research and CrossBow Technology
    NesC programming Language.
    TOSSIM platform for simulations.
    A large component library including network functions and sensor libraries.
    Statically linked, hence no loadable modules.
    No multi threading
  Contiki OS from SİCS
    Multi Threaded,
    Has large support for several platforms (TelosB, MicaZ, etc.)
    Run time module loading.
    TCP/IP and 6LowPAN support
    We will use Contiki in our projects.
  Others
    Java ME for SunSPOT from SUN.
    LiteOS
    And more.

## Slide 19: Thank You for Your Attention.